## Slide 1: ADAS Engineering China Training
[L2 MFC Sense Function – HLA and TSA]
Chassis & Safety | Advanced Driver Assistance Systems

## Slide 2: Training Target
L1 New
L2 Basic
Target Group
(Level of participant before the training)
Help participants to reach skill level 3 Advanced
Know more about functions algorithm and behavior
Training Target
(what can be achieved/gained after having the training)

## Slide 3: Training Agenda
The detection module – LSD(Light Source Detection)
Function introduction – HLA(Head Light Assist)
The detection module – SR(Sign Recognition)
Function introduction – TSA(Traffic Sign Assist)

## Slide 4: HLA Algorithm Architecture

## Slide 5: LSD
Basic recognition will provide the information of lights such as..
  Position
  3D Motion
  Classification
  Pair track information

## Slide 6: LSD

## Slide 7: LSD: Segmentation
The segmentation searches for spots of local brightness maxima in the ROI of the image.
The output of the segmentation is a light object list, with the following information
  Intensity
  RGB-color
  Position
  Size

## Slide 8: Detail of Segmentation (1/3)
Input of segmentation come from imager
  The raw data will provided by the Bayer Pattern
Segmentation finds the high intensity pixels as light objects
  Use red-color only to detect intensity(for performance)
    Skip the non-red data to reduce using the resource.
    To keep the performance with limited hardware resource, kind of filtering need to reduce the memory and calculation.
Step will be Segment by lines -> convert lines to region -> create light object list
Basic classification also calculated
  Basic pair-light estimation
    Only from the intensity and position
R | G | R | G | R
G | B | G | B | G
R | G | R | G | R
G | B | G | B | G
R | G | R | G | R
The image of Bayer Pattern.

## Slide 9: Detail of Segmentation (2/3)
Segment lines:
  Segment each line to segmented line
    Find maxima for each segmented lines
  Intensity leveled for 3 steps. Light is find if the level is changed.
    The threshold of the level will be change after the one cycle of segmentation, to get better segmentation result with different ambient brightness.
    The highest intensity level will be center of light. If same level continues, center of those detected as one light.
0 | 0 | 30 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 60 | 180 | 0 | 0 | 0 | 30 | 30 | 0 | 0
0 | 0 | 30 | 0 | 0 | 30 | 180 | 255 | 30 | 0
0 | 0 | 0 | 0 | 0 | 0 | 80 | 120 | 30 | 0
0 | 0 | 0 | 0 | 0 | 0 | 30 | 0 | 0 | 0
Maxima | Maxima Position | L1 - length | L2- length | L3- length
30 | [2] | 1 |  | 
180,30 | [2],[6] | 2,2 | 1,0 | 
30,255 | [2],[7] | 1,4 | 0,2 | 0,2
120 | [7] | 3 | 1 | 
30 | [6] | 1 |  | 
Intensity
Center of the light
Lv1
Lv2
Lv3
Center of the light
50
100
160
Graph is built from red marked column

## Slide 10: Detail of Segmentation (3/3)
 |  | 180 |  |  |  | 30 |  |  | 
 |  |  |  |  |  |  | 255 |  | 
Convert lines to region:
  Look rows to find the place of light objects.
 |  | 30 |  |  |  |  |  |  | 
 |  | 180 |  |  |  | 30 |  |  | 
 |  | 30 |  |  |  |  | 255 |  | 
 |  |  |  |  |  |  | 120 |  | 
Intensity (blanks are out of calculation)
Create light object list:
  Light object list is separated for each level
  One region will be one light object
Intensity (blanks are out of calculation)
LV1 | 
30 | (6,1)
LV2 | 
Lv3 | 
180 | (2,1)
255 | (7,2)
Intensity
Position
Maxima | Maxima Position | L1 - length | L2- length | L3- length
30 | [2] | 1 |  | 
180,30 | [2],[6] | 2,2 | 1,0 | 
30,255 | [2],[7] | 1,4 | 0,2 | 0,2
120 | [7] | 3 | 1 | 
30 | [6] | 1 |  | 

## Slide 11: LSD: Tracking
The tracking is “observing” the behavior of light objects over time.
Each detected light object is associated with a single light track, based on previous track information.
Light objects without association create new light tracks.
The output of the tracking are light tracks, with following information
  Light object information
  3D-Position (distance)
  Motion (2D/3D)

## Slide 12: Detail of Tracking
Track each light objects over time
  Simple flowchart
Predict tracks
Associate tracks
to lights
Update track infos
Add new track
Dead track flag is set the end of tracking part and will be removed at next frame.
Tracking use the SLAM, the algorithm of tracking estimated from ego motion
Find the similar light object and match to the tracking
  The light near the track will be match
  The characteristic of the light is also important for matching
Association will decide which light to track
  Tracking up to 85
  If the tracking goes to max, the prior light will be tracked
    Priority will be decided by light information (e.g. distance)
Add new pair

## Slide 13: LSD: Analysis
The analysis attaches classification information to light tracks, based on characteristic features, for further detection of
  Vehicles (oncoming or leading traffic)
  City
  Highway
  Tunnel
The output of the analysis are
  Object list
  City data
  Highway data
  Tunnel data

## Slide 14: Detail of Analysis
The vehicle analysis detects oncoming and leading traffic and distinguishes them from reflectors and other active lights such as street lamps.
Each light track is processed in four different stages
  In the base level the basic features for further processing are extracted
  In the 1st level a low level classification is performed on features like intensity, color, motion or temporal behavior
  In the 2nd level a high level classification is performed on features like the shape
  In the 3rd and final level the driving directions of the vehicles are detected

## Slide 15: HLA
The function module interprets the output of the
  Image processing
  Blockage detection
  Current situation, e.g. driving situation
The variant selection control the illumination characteristics of the head lamps depending on the HLA variant
  HLA light
  HLA (standard)
  HLA plus

## Slide 16: HLA Turn Off Reason
HLA has following factories to decide behavior.
  Ambient brightness
  Velocity
  City
  Tunnel
  Object Vehicle
  Blockage

## Slide 17
QUESTIONS

## Slide 18: TSA Algorithm Architecture

## Slide 19: SR
Detection

## Slide 20: SR
Tracking

## Slide 21: SR
Classification

## Slide 22: SR
Afterburner

## Slide 23: SR
Supplementary Sign

## Slide 24: TSA
Traffic Sign Assist is a kind of driver assistance function which makes use of (country-specific) traffic rules to interpret the recognized traffic signs and issues resulting information to the driver (e.g. speed limit cancellation while overtaking is still forbidden).

## Slide 25: TSA
MTS Visualization

## Slide 26
QUESTIONS

## Slide 27: Thank you for your attention!
TRAINER CONTACT INFO:
Name: Yefei Wei
Skype: Yefei, Wei(uia70152)
Office Phone:3916 5785
FEEDBACK:
Please share your feedback by the following link or by scanning the following QR-code:
https://www.wjx.cn/jq/42915896.aspx
Name: Zhongwen Ye
Skype: ye, zhongwen03(uib65042)
Office Phone:3916 5623
Please finish before you leave the class room. Thank you 