## Slide 1: VEHICLE DYNAMICS COMPONENT
Chassis & Safety | Advanced Driver Assistance Systems

## Slide 2: Objective :
Estimate vehicle dynamic signals like Longitudinal velocity , Long Accel, Yaw rate and Lateral Acceleration by Offset compensation and Plausibilization.
Vehicle path prediction by providing Curvature estimation & Motion State detection
Set the DEMs/Errors in case of
a. Invalid inputs
b. Estimated signal / Variance is crossing threshold
c. Input parameters out of range
d. Input signals out of range

## Slide 3: VEHICLE DYNAMICS OBSERVER COMPONENT
The objective of Vehicle Dynamic Observer are ,
a. Filtering and Offset compensation of Sensor Signals
b. Fusion of different sensor signals
c. Path Estimation
d. Set errors when data is not proper.

## Slide 4: VDY Architecture
First layer "Signal processing" is preprocessing the input signals, removes offsets, and supports for each input signal a yaw rate and a corresponding variances
Second layer "State estimation" consists of three modules,:
the yaw rate fusion module using the preprocessed yaw rates,
the velocity estimation
and the motion state estimation
The Last layer "Supplementary data" estimates some additional date based on the information from the above layers, like curve, and lateral acceleration

## Slide 5: VEHICLE DYNAMICS OBSERVER COMPONENT
TRACK WIDTH FRONT
YAW RATE
STEERING WHEEL ANGLE
FOUR WHEEL VELOCITIES
FOUR WHEEL PULSE COUNTER DEVIATION
FOUR WHEEL ROTATION DIRECTION
ACTUAL GEAR POSITION
PARK BRAKE STATE
BRAKE TOURQUE
LONG ACCELERATION
STATIONARY TARGETS VELOCITY
LONG VELOCITY AND ACCELARATION
YAW RATE & Lateral Accel
VEHICLE DYNAMIC OBSERVER
MOTION STATE
VEHICLE CURVATURE
TRACK WIDTH REAR
WHEEL BASE
VEHICLE WEIGHT
CENTER OF GRAVITY HGT
AXLE LOAD DISTR
WHEEL CIRCUMFERENCE
STEERING RATIO
WHEEL TICKS PER REV
UNDERSTEER GRAD
CORNER STIFFNESS
INPUT SIGNALS
INPUT PARAMETERS
OUTPUT SIGNALS
Signal Processing:
a. Yaw Rate
b. Vehicle Velocity
Path Estimation:
a. Curvature
b. Motion State

## Slide 6: Algorithm Architecture
Co-ordinate system:
Autosar Compliant
Defined w.r.t. COG
Left Turn,
SWA +ve
Yaw Rate +ve
Lateral Acc +ve
X
Y
Rear Axle
Front Axle
4. Z +ve up

## Slide 7: INPUT SIGNAL PRE-PROCESSING
1. INPUT SIGNAL MONITOR
Magnitude Limiter
Wheel Speeds +/- 115 m/sec
Yaw Rate +/- 150 deg/sec
Long Accel +/- 10 m/sec2
Lateral Accel - +/10 m/sec2
SWA +/- 90 *SR
Wheel Speeds +/- 10 m/sec
Yaw Rate +/- 6 deg/sec
Long Accel +/- 2.5 m/sec2
Lateral Accel - +/2.5 m/sec2
SWA +/- 6 deg/sec
Rate Limiter
Input Signal
Input Signal
Validity checks
Input Signal
Wait for 3 VDY cycles
To check whether input is INVALID
Then set the state as INVALID

## Slide 8: Inter Connection of Different VDY processing modules

## Slide 9: INPUT SIGNAL PRE-PROCESSING
2.OFFSET COMPENSATION
YAW RATE Offset Compensation
LAT ACCEL Offset Compensation
WHEEL SPEED
Offset Compensation
STEERING WHEEL ANGLE
Offset Compensation
EXT GIER YAW RATE +OFFSET
LAT ACCEL +OFFSET
WHEEL SPEEDS +OFFSET
STEERING WHEEL ANGLE+OFFSET
OFFSET COMPENSATED GIER YAW RATE
OFFSET COMPENSATED LAT ACCEL
OFFSET COMPENSATED WHEEL SPEEDS
OFFSET COMPENSATED STEERING WHEEL ANGLE

## Slide 10: Steering Wheel Angle Offset
When the vehicle is moving at certain velocity
If driver provides SWA as an input
Vehicle develops Yaw rate
Lateral Acceleration is experienced
by the vehicle
Front Wheel Angle
Steer Ratio (Rack and Pinion)
Steering column rotation
sensed by SWA sensor
Angular rotation about z-axis
is sensed by Gyro
Lateral Accelerometer

## Slide 11: Fast Steer Wheel Angle offset computation:
Learning Conditions :
    a. NVM is cleared / New Sensor (Learnt State is zero)
b When the Wheel Speed Difference (FL – FR & RL – RR) is less than
0.6 m/sec and the vehicle velocity > 5 m/sec
c. SWA < 30 deg
d. Collect the samples till distance criteria (> 250 m) is met.
Compute the average of collected samples.
Method of computation :
1. Compute difference between Yaw rate estimated from SWA and
offset compensated Gyro Yaw rate. (Note : Estimated values are
outputs of KFs)
2. SWA Offset = Difference * SR * (L + EG * Vx2)/Vx
3. Set the Learnt State to 1

## Slide 12: SWA Offset Overview
Learning distance Criteria :
Fast steer wheel angle --- 250 cycles
First Learning --- 25 Km
Second Learning --- 30 Km
Third Learning -- - 35 km
Fourth Learning ---- 40 Km
Fifth Learning ---- 40 km
Sixth Learning ----- 50 Km
Reset Criteria:
Impact of SWA offset :
It will have impact on curvature computation
Errors associated with SWA offset :
Out of Range SWA offset error (SwaOffsRg)
If there is a difference more than 0.5 deg between previously learnt value and the latest value then update that value with the latest value and set the state to 4.
(learned but not confirmed)
(learned and confirmed once)
(learned and confirmed twice)

## Slide 13: Next Level SWA offset Learning
Learning conditions : (Straight drive)
Velocity > 10 m/sec, Wheel Speed Difference (FL – FR & RL – RR) is less than 0.3 m/sec
-14 deg
14 deg
Build Histogram : Histogram is filled based on direct SWA measurements
Check enough number of samples are collected based on distance criteria.
Computed median, once enough number of samples are collected.
W1
W5
W15
Lateral Acceleration is more than 1.8 m/sec2
Reset histogram.

## Slide 14: SWA Offset Overview
Learning distance Criteria :
Fast steer wheel angle --- 250 cycles
First Learning --- 25 Km
Second Learning --- 30 Km
Third Learning -- - 35 km
Fourth Learning ---- 40 Km
Fifth Learning ---- 40 km
Sixth Learning ----- 50 Km
Reset Criteria:
Impact of SWA offset :
It will have impact on curvature computation
Errors associated with SWA offset :
Out of Range SWA offset error (SwaOffsRg)
If there is a difference more than 0.5 deg between previously learnt value and the latest value then update that value with the latest value and set the state to 4.
(learned but not confirmed)
(learned and confirmed once)
(learned and confirmed twice)

## Slide 15: YAW RATE OFFSET
When the vehicle is detected to be in stand still state, yaw rate stand still offset is estimated
as mean value of 30 cycles for the first time. Later on it is computed as a mean of 15 cycles.
Quality of yaw rate offset determines the last estimated yaw rate offset will be considered for
compensation or not.
The allowed learning is 4 deg/sec in a stand still cycle.
Turn Table Detection :
When the motion state detected is stand still and if the measured yaw rate is more than
7 deg/sec
Fast Stand Still : When the quality is less than 0.75 (approximately)
Dynamic Yaw rate offset : (High way driving)
a. Long Vel >=14 m/sec, Lateral Accel <=3.5 m/sec2, Long Accel <= 2.0 m/sec2, Yaw Rate Front and Rear Diffe <=0.02
b. Initial value of the dynamic yaw rate offset is Stand Still offset and its starts learning on top of that. The learning rate is not
allowed to go more than 0.002 in 500 cycles.

## Slide 16: Lateral Accel Offset Learning (Similar lines of SWA offset)
Learning conditions : (Straight drive)
Velocity > 10 m/sec, Wheel Speed Difference (FL – FR & RL – RR) is less than 0.3 m/sec.
-2.5 m/sec2
2.5 m/sec2
Build Histogram : Histogram is filled based on direct SWA measurements
Check enough number of samples are collected based on distance criteria.
Compute median, once enough number of samples are collected.
W1
W5
W15
(Distance Computation)

## Slide 17: Lateral Acceleration Offset
Learning distance Criteria :
First Learning --- 20 Km
Second Learning --- 25 Km
Third Learning -- - 30 km
Fourth Learning ---- 30 Km
Reset Criteria:
Lateral Acceleration more than 1.8 m/sec2
Errors associated with SWA offset :
Out of Range lateral acceleration offset error (AyOffsRg)

## Slide 18: YAW RATE ESTIMATION
GYE
KALMAN FILTER
SYE
KALMAN FILTER
AYE
KALMAN FILTER
WYE
KALMAN FILTER
OFFSET COMPENSATED GIER YAW RATE
OFFSET COMPENSATED STEERING WHEEL ANGEL
OFFSET COMPENSATED LATERAL ACCELERATION
OFFSET COMPENSATED
4 WHEEL VELOCITIES
YAW RATE
+VARIANCE
MERGED YAW RATE +VARIANCE
STEERING WHEEL YAW RATE
+VARIANCE
LAT ACCEL YAW RATE
+VARIANCE
WHEEL SPD YAW RATE
+VARIANCE
KALMAN FILTER
YE

## Slide 19: VELOCITY ESTIMATION
OFF COMP WHEEL VELOCITY FRONT LEFT
OFF COMP WHEEL VELOCITY FRONT RIGHT
OFF COMP WHEEL VELOCITY REAR LEFT
OFF COMP WHEEL VELOCITY REAR RIGHT
MERGED VELOCITY +VARIANCE
MERGING KALMAN FILTER
VELOCITY CORRECTION
CORRECETD VELOCITY VARIANCE
MERGED ACCEL +VARIANCE
RELAVTIVE VELOCITY+ VAR FROM STATIONARY TARGETS

## Slide 20: CF computation
Build histogram from the ratio of speeds (CF).
Compute median from histogram to compute CF statistically
Range of CF = 0.7 to 1.3

## Slide 21: VDY CURVE ESTIMATION
Curve Estimation using Kalman Filter
Vehicle Velocity
Steering wheel Curve
Yaw Rate Curve
External Velocity
Steering wheel Angle
Steering wheel Angle
Wheel Speeds
Gier Yaw Rate
Lateral Acceleration
Vehicle Curve/Lane Radius
VDY Internal Data
VDY Input
VDY Output
Yaw Rate

## Slide 22: MOTION STATE ESTIMATION
WHEEL PULSE COUNTER PROCESSING
VEHICLE VELOCITY PROCESSING
YAW RATE PROCESSING
WHEEL DIRECTION PROCESSING
BRAKE TORQUE
PROCESSING
GEAR SHIFT
PROCESSING
PARK BRAKE
PROCESSING
BAYES NET
VEHICLE MOTION STATE
-FORWARD
-REVERSE
-STANDSTIL
-MOVING

## Slide 23: Mtn State Detection

## Slide 24: VDY Outputs
Yaw Rate
Lateral Acceleration
Long Velocity & Accel
Motion State
Curvature
SWA
Uncorrected Veh Velocity
Corrected Veh Velocity
Corrected Velocity Variance
Vehicle Acceleration
Quality of Velocity
Quality of Accel
Offset compensated SWA
SWA offset
Yaw rate
Yaw rate variance
Yaw rate Offset
Yaw rate Quality
Lateral Acceleration
Lateral Acceleration offset
Lateral Acceleration Quality
Motion State
Motion State Confidence
Curvature
Driver Intended curvature

## Slide 25: VDY-MTS simulation (Interface)
VDY-Algo
R
T
E
R
T
E
R T E
R T E
Input
interface
Output
interface
Parameter
interface
NVM
interface
MTS
S
I
M
A
D
A
P
T
E
R
RECORDING
DEVICE
VISUAL
PLOTS
ECU-CODE
Simulation
Results

## Slide 26: VDY-Structures in MTS

## Slide 27: VDY-Structures in MTS

## Slide 28
Thank you